ANTENNAS
York County Amateur Radio Club 2023/2/05
n1xp
[Speaker Notes: MANY KINDS AND TYPES OF ANTENNAS DIPOLE IS THE BASIS OF ANTENNA AND SHOULD BE UNDERSTOOD ANTENNA DEFINITION]

---
KRAUS DEFINES A RADIO ANTENNA AS “THE STRUCTURE ASSOCIATED WITH THE REGION OF TRANSITION BETWEEN A GUIDED WAVE AND A FREE-SPACE WAVE, OR VICE VERSA.” [1]
BASIC COMPONENT OF ANY ELECTRONIC SYSTEM WHICH DEPENDS ON FREE SPACE AS THE PROPAGATION MEDIUM
THE CONNECTING LINK BETWEEN FREE SPACE AND TRANSMITTER OR RECEIVER
RECIPROCAL PROPERTIES
RECEIVES OR TRANSMITS EQUALLY
BASIC PROPERTIES
IMPEDANCE
GAIN
RADIATION PATTERN
POLARIZATION

---
CAN TAKE MANY DIFFERENT FORMS
SOME WORK BETTER THAN OTHERS
Classic Dipole
End Fed
Wire on Ground

---
VERTICAL λ/4 WAVE - WITH MULTIPLE RADIALS
IMAGE
[Speaker Notes: NOTICE COUNTERPOISE OF RADIALS AM BROADCASTERS HAVE A MINIMUM OF 120 1/4-WAVE RADIALS - SOME LOCATIONS MUST HAVE MORE]

---
USUALLY A THIN CONDUCTOR ARRANGED IN A LINEAR CONFIGURATION
EXAMPLE = HALF-WAVE DIPOLE
Dipole = “di”, meaning two; “pole” meaning electrical polarity
{ %lambda } over {2}
{ %lambda } over {2}
TRANSMISSION LINE
TRANSMISSION LINE
{ %lambda } over { 2 } = { 468 } over { f_{MHz}}

---
THE “IDEAL” ANTENNA RADIATES 100% OF
THE ENERGY DELIVERED TO IT
THE IDEAL ANTENNA DOES NOT EXIST

---
SIMPLE THEORETICAL ANTENNA CIRCUIT ANALYSIS [2]
RR
RG
AT RESONANCE
RR = RADIATION RESISTANCE RG = GROUND LOSSES
RR
RG
jXR
jXR = REACTANCE LOSS
NON- RESONANCE
[Speaker Notes: Important to reduce ground losses, Rg, as much as possible Ohms Law: The smaller Rg, the more energy across Rr = better efficiency Adding a Reactive component further reduces efficiency MOST ANTENNAS HAVE A REACTIVE COMPONENT]

---
FEED-POINT IMPEDANCE OF HALF-WAVE DIPOLE ≈72Ω IN FREE SPACE
ASSUMES HALF-WAVE ABOVE EARTH
FEED-POINT IMPEDANCE OF QUARTER-WAVE VERTICAL ≈ 37Ω
ASSUMES GOOD CONDUCTING EARTH AND ADEQUATE # OF RADIALS
A GROUND ROD IS NOT SUFFICIENT – A DC GROUND IS NOT AN “RF GROUND”
THE FEED-POINT IMPEDANCE OF A HORIZONTAL λ/2-DIPOLE STEADILY DECREASES AS THE ANTENNA IS LOWED BELOW λ/4-WAVELENGTH ABOVE GROUND
THE FEED POINT IMPEDANCE OF A λ/2-DIPOLE STEADILY INCREASES AS THE FEED POINT IS MOVED FROM THE CENTER TOWARDS AN END

---
RESONANT HALF-WAVE DIPOLE STANDING WAVES - λ/4 ABOVE EARTH
Z = Impedance
I = Current
Feed Point
E = Voltage
Z= {E} over {I}
`
[Speaker Notes: Center Impedance ~72~ 75ohms Z is ratio of Voltage to Current Polarity of V & I changes with each half cycle Z approaches 2500~3000ohms at the ends]

---
½-wave Dipole
Horizontal Plane
Mounted 1/2-wave
Above perfect earth
[Speaker Notes: RADIATION PATTERN]

---
HALF-WAVE DIPOLE
VERTICAL PLANE
[Speaker Notes: The colors represent different heights above ground]

---
HORIZONTAL WIRE ANTENNA TAKE-OFF ANGLE
[3]
TOA = sin ^{ -1 } ({ %lambda } over { 4h })
λ = Wavelength
h = Height above ground	(both in meters)
[Speaker Notes: Take-off angle is the angle, with respect to ground, of the major radiating lobe The lower the angle - the longer the skip distanced]

---
MULTI-BAND ANTENNAS
VHF LOG PERIODIC
VERTICAL POLARIZATION
HF MULTI-BAND BEAM
HORIZONTAL POLARIZATION
BASICALLY DIPOLES WITH PARASITIC ELEMENTS
[Speaker Notes: Yagi Yagi-Uda beam antennas Basically a dipole with “parasitic” or un-connected elements Left: Vertically polarized, VHF/UHF beam Right: Horizontally POLARIZED HF multi-band beam.]

---
BROADBAND “CAGE” DIPOLE
SINGLE WIRE DIPOLES HAVE VERY NARROW RESONANT BANDWIDTH
BROADEN FREQUENCY RANGE BY MAKING A “CAGE” OF WIRES
MANY VARIATIONS – FAN DIPOLE FOR EXAMPLE

---
80/75 METER DIPOLE VSWR CURVES
BROADBAND DIPOLE
NORMAL “THIN WIRE” DIPOLE

---
MULTI-BAND “WINDOM”
OFF-CENTER FED DIPOLE
EVEN HARMONICALLY RELATED BANDS i.e., 80m, 40m, 20m, 10m
[Speaker Notes: Harmonically related i.e., 1f, 2f, 3f, 4f, etc If constructed for 80meters then will operate on 40m, 20, 10m Note 15meters and WARC bands are not integer harmonics of 80m.]

---
“ZEPP” MULTI-BAND ANTENNA
{%lambda} over {2}
First used in Zepplin Airships, 1907
Antenna problems
High losses incurred unless mounted ¼-wavelength above earth
Coupling system must include some harmonic-attenuating filtering because the antenna has no discrimination against harmonics
Has high RF Voltage at feed-point
Requires Matching network for all bands
OPEN FEED LINE
{%lambda} over {4}
[Speaker Notes: High Z at feed point High V at feed point Requires complex matching network]

---
END-FED HALF-WAVE ANTENNA “EFHW”
GIMMICKY!
CUTE
49:1 Balun
{%lambda} over {2}
COUNTERPOISE
EASY TO INSTALL
Z ≈ 2500 Ohms
2500 ÷ 50 ≈ 49
1:1 Line Choke
LOW COST
Coax to Lightning Arrestor & Antenna Matching Network
IS IT A GOOD ANTENNA?
[Speaker Notes: Gimmicky! Cute! Fad! Low Cost! LOW COST BASICALLY A WRONGLY-CONFIGURED OFF CENTER FED DIPOLE LET’S LOOK AT EFHW RADIATION PATTERNS]

---
EFHW ANTENNA RADIATION PATTERNS
( w/ BALUN & LINE CHOKE, ≈1/2 λ Above Earth)

---
EFHW ANTENNA RADIATION PATTERNS
(Sloping – 6ft-to-23ft,
w/Counterpoise & Line Choke)

---
END-FED HALF-WAVE ANTENNA “EFHW”
WIDE REPUTATION “FINICKY”, WON’T LOAD, POSITION SENSITIVE, NEEDS A TUNER, RF IN THE SHACK
Balun secondary COUNTERPOISE is a requirement: - RF current flow in a conductor in concert with the oscillatory electric field causes Electromagnetic Radiation (ala Mr. Maxwell) and the transmitter does not “create” current from nothing, even in the secondary (ala Mr. Kirchhoff).
Ground losses MUST be minimized! - Wastes transmitter power because ground losses are in series with the antenna radiation resistance (ala Mr. Ohm).
Coax shield (or your body/radio) and lossy soil completes the circuit
BALUN ABSORBS 12% OF TRANSMITTER POWER BECAUSE OF HIGH REACTANCE COMPONENT
NO GAIN OVER 1/2-WAVE DIPOLE

---
40-METER (68’) END-FED HALF-WAVE ANTENNA
1/4-WAVE ABOVE PERFECT EARTH
w/BALUN & LINE CHOKE
[Speaker Notes: VSWR CURVE NOT PROMISING EITHER OF COURSE YOUR MILEAGE MAY VARY]

---
DOUBLE EXTENDED ZEPP
GREAT DX WIRE ANTENNA
Must be mounted 1/4λ above ground (80m = 68’)
Multi-band – must use matching Network
[Speaker Notes: Requires substantial Real Estate 80m DEZ is ~~300ft long Bi-directional]

---
PRACTICAL DOUBLE EXTENDED ZEPP
`
.64 {%lambda}
.64 {%lambda}
{%lambda} over {4}
MATCHING
NETWORK

---
TERMINATED FOLDED DIPOLE “TFD”
MULTI-BAND
[Speaker Notes: A true multi-band HF Antenna Will operate with VSWR of <3:1 across HF spectrum. Some designs differ in dimension “W” and terminating resistance value.]

---
MULTI-BAND DIPOLE
[Speaker Notes: More bands may be added]

---
CAROLINA WINDOM® [4]
DISTANT COUSIN OF THE G5RV
“UPSIDE-DOWN VERTICAL”
OCF WIRE IS COUNTERPOISE
22’ COAX IS VERTICAL RADIATOR
OMNI DIRECTIONAL PATTERN
LOW ANGLE OF RADIATION
VERY LITTLE GROUND LOSSES

---
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
NOT AN ANTENNA OR ANTENNA SYSTEM
NVIS IS A MODE OF HF PROPAGATION
BEST FOR LOCAL and REGIONAL HF COMMUNICATIONS – NOT DX
DIRECTIVITY PATTERN MAXIMIZES TRANSMISSION AND RECEPTION AT HIGH ANGLES
REJECTS LOW ANGLE, LONG RANGE, NOISE
USED BY MILITARY, FEMA, US CORPS of ENGINEERS, RED CROSS, MARS, SHARES, ARES/RACES
[Speaker Notes: YORK CO VIRGINIA HURRICANE SANDY OCT 27 2012 HIT NEW JERSEY OCT 29]

---
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
[6]
[5]
HORIZONTAL DIPOLE AT HEIGHT ≤ 0.2λ
EFFICIENCY DROPS AS HEIGHT DECREASED < 0.15λ
[Speaker Notes: YORK CO VIRGINIA HURRICANE SANDY OCT 27 2012 HIT NEW JERSEY OCT 29]

---
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
[7]

---
[8]

---
What is wrong in this diagram from
February 2023 QST?
NO COUNTERPOISE
NO LIGHTNING ARRESTOR
NO GROUNDING & BONDING
Unlimited access to “HOT” Antenna wire
In QST’s defense, another figure “mentions” a counterpoise but offers no details
[Speaker Notes: I built it just like in QST Don’t believe everything you see - Antenna “grounding” is different from electrical safety G&B Grounding & bonding will be the topic for next month.]

---
SAFETY FIRST

---
[1]	Kraus, John D., “ANTENNAS”, McGraw-Hill Book Company, Inc., 1950
[2]	Jasik, Henry, Editor, “ANTENNA ENGINEERING HANDBOOK”, McGraw-Hill Book Company, 1961
[3]	Freeman, Roger L., “Telecommunications Transmission Hanbook, 2nd Ed., John Wiley & Sons, 1981
[4]	Jim Wilkie (WY4R), Edgar Lambert (WA4LVB), and Joe Wright (W4UEB), “The ARRL Antenna Book” 1997
Staw, R Dean; Editor
[5]	Ben A. Witvliet, Erik van Maanen , George J. Petersen, Albert J. Westenberg, Mark J. Bentum,	Cornelis H. Slump, and Roel Schiphorst, “Near Vertical Incidence Skywave Propagation: Elevation Angles	and Optimum Antenna Height for Horizontal Dipole Antennas”, IEEE Antennas and Propagation Magazine,	Vol. 57, No. 1, February 2015
[6]	Ibid.
[7]	Ibid.
[8]	Ibid.
Paper referenced in [5, 6, 7 & 8] is available on the club web site: https://w1yca.org/ant.html