## Slide 1
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
Notes: MANY KINDS AND TYPES OF ANTENNAS
DIPOLE IS THE BASIS OF ANTENNA AND SHOULD BE UNDERSTOOD
ANTENNA DEFINITION

## Slide 2
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
KRAUS DEFINES A RADIO ANTENNA AS “THE STRUCTURE ASSOCIATED WITH THE REGION OF TRANSITION BETWEEN A GUIDED WAVE AND A FREE-SPACE WAVE, OR VICE VERSA.” [1]
BASIC COMPONENT OF ANY ELECTRONIC SYSTEM WHICH DEPENDS ON FREE SPACE AS THE PROPAGATION MEDIUM
THE CONNECTING LINK BETWEEN FREE SPACE AND TRANSMITTER OR RECEIVER
RECIPROCAL PROPERTIES
  RECEIVES OR TRANSMITS EQUALLY
BASIC PROPERTIES
  IMPEDANCE
  GAIN
  RADIATION PATTERN
  POLARIZATION

## Slide 3
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
CAN TAKE MANY DIFFERENT FORMS
  SOME WORK BETTER THAN OTHERS
Classic Dipole
End Fed
Wire on Ground

## Slide 4
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
VERTICAL λ/4 WAVE - WITH MULTIPLE RADIALS
IMAGE
Notes: NOTICE COUNTERPOISE OF RADIALS
AM BROADCASTERS HAVE A MINIMUM OF 120 1/4-WAVE RADIALS - SOME LOCATIONS MUST HAVE MORE

## Slide 5
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
USUALLY A THIN CONDUCTOR ARRANGED IN A LINEAR CONFIGURATION
  EXAMPLE = HALF-WAVE DIPOLE
  Dipole = “di”, meaning two; “pole” meaning electrical polarity
TRANSMISSION LINE
TRANSMISSION LINE

## Slide 6
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
THE “IDEAL” ANTENNA RADIATES 100% OF
THE ENERGY DELIVERED TO IT
THE IDEAL ANTENNA DOES NOT EXIST

## Slide 7
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
RR
RG
AT RESONANCE
RR = RADIATION RESISTANCE RG = GROUND LOSSES
SIMPLE THEORETICAL ANTENNA CIRCUIT ANALYSIS [2]
RR
RG
jXR
jXR = REACTANCE LOSS
NON- RESONANCE
Notes: Important to reduce ground losses, Rg, as much as possible
Ohms Law: The smaller Rg, the more energy across Rr = better efficiency
Adding a Reactive component further reduces efficiency
MOST ANTENNAS HAVE A REACTIVE COMPONENT

## Slide 8
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
FEED-POINT IMPEDANCE OF HALF-WAVE DIPOLE ≈72Ω IN FREE SPACE
  ASSUMES HALF-WAVE ABOVE EARTH
FEED-POINT IMPEDANCE OF QUARTER-WAVE VERTICAL ≈ 37Ω
  ASSUMES GOOD CONDUCTING EARTH AND ADEQUATE # OF RADIALS
  A GROUND ROD IS NOT SUFFICIENT – A DC GROUND IS NOT AN “RF GROUND”
THE FEED-POINT IMPEDANCE OF A HORIZONTAL λ/2-DIPOLE STEADILY DECREASES AS THE ANTENNA IS LOWED BELOW λ/4-WAVELENGTH ABOVE GROUND
THE FEED POINT IMPEDANCE OF A λ/2-DIPOLE STEADILY INCREASES AS THE FEED POINT IS MOVED FROM THE CENTER TOWARDS AN END

## Slide 9
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
E = Voltage
I = Current
Feed Point
`
Z = Impedance
RESONANT HALF-WAVE DIPOLE STANDING WAVES - λ/4 ABOVE EARTH
Notes: Center Impedance ~72~ 75ohms
Z is ratio of Voltage to Current
Polarity of V & I changes with each half cycle
Z approaches 2500~3000ohms at the ends

## Slide 10
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
½-wave Dipole
Horizontal Plane
Mounted 1/2-wave
Above perfect earth
Notes: RADIATION PATTERN

## Slide 11
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
HALF-WAVE DIPOLE
VERTICAL PLANE
Notes: The colors represent different heights above ground

## Slide 12
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
HORIZONTAL WIRE ANTENNA TAKE-OFF ANGLE
[3]
λ = Wavelength
h = Height above ground (both in meters)
Notes: Take-off angle is the angle, with respect to ground, of the major radiating lobe
The lower the angle - the longer the skip distanced

## Slide 13
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
MULTI-BAND ANTENNAS
VHF LOG PERIODIC
VERTICAL POLARIZATION
HF MULTI-BAND BEAM
HORIZONTAL POLARIZATION
BASICALLY DIPOLES WITH PARASITIC ELEMENTS
Notes: Yagi Yagi-Uda beam antennas Basically a dipole with “parasitic” or un-connected elements
Left: Vertically polarized, VHF/UHF beam
Right: Horizontally POLARIZED HF multi-band beam.

## Slide 14
ANTENNAS
BROADBAND “CAGE” DIPOLE
York County Amateur Radio Club 2023/2/05
n1xp
SINGLE WIRE DIPOLES HAVE VERY NARROW RESONANT BANDWIDTH
BROADEN FREQUENCY RANGE BY MAKING A “CAGE” OF WIRES
MANY VARIATIONS – FAN DIPOLE FOR EXAMPLE

## Slide 15
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
80/75 METER DIPOLE VSWR CURVES
NORMAL “THIN WIRE” DIPOLE
BROADBAND DIPOLE

## Slide 16
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
MULTI-BAND “WINDOM”
OFF-CENTER FED DIPOLE
EVEN HARMONICALLY RELATED BANDS i.e., 80m, 40m, 20m, 10m
Notes: Harmonically related i.e., 1f, 2f, 3f, 4f, etc
If constructed for 80meters then will operate on 40m, 20, 10m
Note 15meters and WARC bands are not integer harmonics of 80m.

## Slide 17
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
“ZEPP” MULTI-BAND ANTENNA
OPEN FEED LINE
First used in Zepplin Airships, 1907
Antenna problems
  High losses incurred unless mounted ¼-wavelength above earth
  Coupling system must include some harmonic-attenuating filtering because the antenna has no discrimination against harmonics
  Has high RF Voltage at feed-point
  Requires Matching network for all bands
Notes: High Z at feed point
High V at feed point
Requires complex matching network

## Slide 18
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
END-FED HALF-WAVE ANTENNA “EFHW”
COUNTERPOISE
49:1 Balun
1:1 Line Choke
Coax to Lightning Arrestor & Antenna Matching Network
Z ≈ 2500 Ohms
2500 ÷ 50 ≈ 49
GIMMICKY!
CUTE
EASY TO INSTALL
IS IT A GOOD ANTENNA?
LOW COST
Notes: Gimmicky! Cute! Fad! Low Cost! LOW COST
BASICALLY A WRONGLY-CONFIGURED OFF CENTER FED DIPOLE
LET’S LOOK AT EFHW RADIATION PATTERNS

## Slide 19
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
EFHW ANTENNA RADIATION PATTERNS
( w/ BALUN & LINE CHOKE, ≈1/2 λ Above Earth)

## Slide 20
ANTENNAS
EFHW ANTENNA RADIATION PATTERNS
(Sloping – 6ft-to-23ft,
w/Counterpoise & Line Choke)
York County Amateur Radio Club 2023/2/05
n1xp

## Slide 21
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
END-FED HALF-WAVE ANTENNA “EFHW”
WIDE REPUTATION “FINICKY”, WON’T LOAD, POSITION SENSITIVE, NEEDS A TUNER, RF IN THE SHACK
Balun secondary COUNTERPOISE is a requirement: - RF current flow in a conductor in concert with the oscillatory electric field causes Electromagnetic Radiation (ala Mr. Maxwell) and the transmitter does not “create” current from nothing, even in the secondary (ala Mr. Kirchhoff).
Ground losses MUST be minimized! - Wastes transmitter power because ground losses are in series with the antenna radiation resistance (ala Mr. Ohm).
Coax shield (or your body/radio) and lossy soil completes the circuit
BALUN ABSORBS 12% OF TRANSMITTER POWER BECAUSE OF HIGH REACTANCE COMPONENT
NO GAIN OVER 1/2-WAVE DIPOLE

## Slide 22
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
40-METER (68’) END-FED HALF-WAVE ANTENNA
1/4-WAVE ABOVE PERFECT EARTH
w/BALUN & LINE CHOKE
Notes: VSWR CURVE NOT PROMISING EITHER
OF COURSE YOUR MILEAGE MAY VARY

## Slide 23
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
DOUBLE EXTENDED ZEPP
GREAT DX WIRE ANTENNA
Must be mounted 1/4λ above ground (80m = 68’)
Multi-band – must use matching Network
Notes: Requires substantial Real Estate
80m DEZ is ~~300ft long
Bi-directional

## Slide 24
`
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
PRACTICAL DOUBLE EXTENDED ZEPP
MATCHING
NETWORK

## Slide 25
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
TERMINATED FOLDED DIPOLE “TFD”
MULTI-BAND
Notes: A true multi-band HF Antenna
Will operate with VSWR of <3:1 across HF spectrum.
Some designs differ in dimension “W” and terminating resistance value.

## Slide 26
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
MULTI-BAND DIPOLE
Notes: More bands may be added

## Slide 27
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
CAROLINA WINDOM® [4]
DISTANT COUSIN OF THE G5RV
“UPSIDE-DOWN VERTICAL”
OCF WIRE IS COUNTERPOISE
22’ COAX IS VERTICAL RADIATOR
  OMNI DIRECTIONAL PATTERN
  LOW ANGLE OF RADIATION
  VERY LITTLE GROUND LOSSES

## Slide 28
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
NOT AN ANTENNA OR ANTENNA SYSTEM
NVIS IS A MODE OF HF PROPAGATION
BEST FOR LOCAL and REGIONAL HF COMMUNICATIONS – NOT DX
DIRECTIVITY PATTERN MAXIMIZES TRANSMISSION AND RECEPTION AT HIGH ANGLES
REJECTS LOW ANGLE, LONG RANGE, NOISE
USED BY MILITARY, FEMA, US CORPS of ENGINEERS, RED CROSS, MARS, SHARES, ARES/RACES
Notes: YORK CO VIRGINIA
HURRICANE SANDY OCT 27 2012
HIT NEW JERSEY OCT 29

## Slide 29
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
HORIZONTAL DIPOLE AT HEIGHT ≤ 0.2λ
EFFICIENCY DROPS AS HEIGHT DECREASED < 0.15λ
[5]
[6]
Notes: YORK CO VIRGINIA
HURRICANE SANDY OCT 27 2012
HIT NEW JERSEY OCT 29

## Slide 30
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS

## Slide 31
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
NVIS
NEAR-VERTICAL-INCIDENT-SKYWAVE
[7]

## Slide 32
ANTENNAS
York County Amateur Radio Club 2023/2/05
n1xp
[8]

## Slide 33
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS

## Slide 34
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
What is wrong in this diagram from
February 2023 QST?
NO COUNTERPOISE
NO LIGHTNING ARRESTOR
NO GROUNDING & BONDING
Unlimited access to “HOT” Antenna wire
In QST’s defense, another figure “mentions” a counterpoise but offers no details
Notes: I built it just like in QST
Don’t believe everything you see -
Antenna “grounding” is different from electrical safety G&B
Grounding & bonding will be the topic for next month.

## Slide 35
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
SAFETY FIRST

## Slide 36
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS
[1] Kraus, John D., “ANTENNAS”, McGraw-Hill Book Company, Inc., 1950
[2] Jasik, Henry, Editor, “ANTENNA ENGINEERING HANDBOOK”, McGraw-Hill Book Company, 1961
[3] Freeman, Roger L., “Telecommunications Transmission Hanbook, 2nd Ed., John Wiley & Sons, 1981
[4] Jim Wilkie (WY4R), Edgar Lambert (WA4LVB), and Joe Wright (W4UEB), “The ARRL Antenna Book” 1997
Staw, R Dean; Editor
[5] Ben A. Witvliet, Erik van Maanen , George J. Petersen, Albert J. Westenberg, Mark J. Bentum, Cornelis H. Slump, and Roel Schiphorst, “Near Vertical Incidence Skywave Propagation: Elevation Angles and Optimum Antenna Height for Horizontal Dipole Antennas”, IEEE Antennas and Propagation Magazine, Vol. 57, No. 1, February 2015
[6] Ibid.
[7] Ibid.
[8] Ibid.
Paper referenced in [5, 6, 7 & 8] is available on the club web site: https://w1yca.org/ant.html

## Slide 37
York County Amateur Radio Club 2023/2/05
n1xp
ANTENNAS